ITEM DESCRIPTION

1.0	The purpose of this requirement is to Purchase Spiral Duct Hose.

2.0	Item Description/Quantity:

| Item Number: | 0001 |
| --- | --- |
| Item Name: | Spiral Duct Hose |
| Manufacturer Name: | National Marine Plastic Co., Ltd. |
| Production/Model Number: | NM-SP7-5-75-180GX |
| Specification: | 7 inch x 16 feet long (see below salient characteristics) |
| Quantity: | Forty (40) each |

The Government accepts as equal product with following salient physical, functional and other characteristics.

| (1) (2) (3) (4) (5) (6) (7) (8) (9) (10) (11) (12) (13) (14) (15) (16) | Duct hose (7”ID x 16’L x 30mm Pitch) Quantity: 40 each Dimensions shall be in accordance with Enclosure. Material: Frame retardant polyester and antistatic cloth Color: Gray (lattice pattern) Size: 7”ID, 16’L (Acceptable Tolerance: +/-10%) Weight: 20kg (Acceptable Tolerance: +/-10%) Sheet Thickness: 0.41mm (Acceptable Tolerance: +/-10%) Spiral Pitch: 30mm (Acceptable Tolerance: +/-10%) Spiral wire: 2.9mm Dia. x 6C hard steel wire (or equal) Connection type: YKK No.10 (or equal) Without Pull Tab Fastener and 3mmD hard steel (or equal) - Piano wire 10mm (Acceptable Tolerance: +/-10%) inside of sewed point (Side A) and YKK No.10 (or equal) - Pull Tab Fastener with leak prevention (Side B) - Sewing point: 10mm from outside and 30mm from the end of spiral wire adapter (Acceptable Tolerance: +/-10%) Ground: Red insulated Alligator Clip with 3mmD x 300mmL wire (Acceptable Tolerance: +/- 10%) (Fixation method: Bolt nut and rivet combinations) - Protector: Ohm tape (Ω type) Lifting component: 3pieces for each side Fastener Stopper: 150mmL X 15mmW Nylon belt (Acceptable Tolerance: +/-10%) with button on the end of Side B Fastener. (Color: Moss Green) Woven Printed Label “FR” on both fastener mounts Red stenciled Wind-Direction on Side B |
| --- | --- |

The Government accepts following products as equal characteristics and the level of quality.

| Manufacturer | Production/Model Number |
| --- | --- |
| N/A | N/A |

3.0	Reference / Enclosures: N/A

4.0	Ancillary Works and/or Other Requirements: N/A

5.0	Delivery Location:

N45598, SRF AND JRMC DET SASEBO

U. S. NAVAL BASE SASEBO, Bldg#487

Tategami-Cho, Mu Banchi, Sasebo City, 857-0056

POC: Hikaru Ooba

Command/Ship: SRF JRMC DET Sasebo

6.0	Deliver Date:

(The Government request delivery date (RDD) is 40 days after receive order (ARO).  Actual delivery date will be specified upon award.)

7.0	Note:

7.1	Government POC: will be provided upon award

| Technical POC | Contracting POC |
| --- | --- |
| Will be provided upon award | Name: Akira Hayashida Title: Contract Specialist TEL: 070-7416-3004 E-mail: Akira.hayashida.ja@fe.navy.mil |

7.1.1	Only the Government Technical POC has authority to coordinate schedule with the contractor within terms and conditions of this contract.  The Government Technical POC will coordinate base access and provide escorts for the contractor if escorts are required for personnel entering, departing, and working in required areas.

7.1.2	Only the Contracting Officer and/or designated Contracting POC have authority to change any terms and conditions of this contract.  Report any conditions, discrepancies, and/or finding to the Contracting POC via the Government Technical POC.

(End of Item Description)